Trellises

3-Part Specification

Cable/ Rod Trellis Systems

12345Section NameProject NameProject Number

GENERAL NOTES TO SPECIFIER: THIS SPECIFICATION SECTION HAS BEEN PREPARED TO ASSIST DESIGN PROFESSIONALS IN THE PREPARATION OF PROJECT OR OFFICE MASTER SPECIFICATIONS. IT FOLLOWS GUIDELINES ESTABLISHED BY THE CONSTRUCTION SPECIFICATIONS INSTITUTE, AND THEREFORE MAY BE USED WITH MOST MASTER SPECIFICATION SYSTEMS WITH MINOR EDITING. EDIT CAREFULLY TO SUIT PROJECT REQUIREMENTS. MODIFY AS NECESSARY AND DELETE ITEMS THAT ARE NOT APPLICABLE. VERIFY THAT REFERENCED SECTION NUMBERS AND TITLES ARE CORRECT. (NUMBERS AND TITLES REFERENCED ARE BASED ON MASTERFORMAT, 2004 EDITION). THIS SECTION ASSUMES THE PROJECT MANUAL WILL CONTAIN COMPLETE DIVISION 1 DOCUMENTS INCLUDING 01 25 13(PRODUCT SUBSTITUTION PROCEDURES, SECTIONS 01 33 00(SUBMITTAL PROCEDURES, 01 62 00(PRODUCT OPTIONS, 01 66 00(PRODUCT STORAGE AND HANDLING REQUIREMENTS, 01 74 00(CLEANING AND WASTE MANAGEMENT, 01 77 00(CLOSEOUT PROCEDURES, AND 01 78 00(CLOSEOUT SUBMITTALS. CLOSE COORDINATION WITH DIVISION 1 SECTIONS IS REQUIRED. IF THE PROJECT MANUAL DOES NOT CONTAIN THESE SECTIONS, ADDITIONAL INFORMATION SHOULD BE INCLUDED UNDER THE APPROPRIATE ARTICLES. THIS IS AN OPEN PROPRIETARY SPECIFICATION ALLOWING USERS THE OPTION OF APPROVING OTHER MANUFACTURERS THAT COMPLY WITH THE CRITERIA SPECIFIED HEREIN. NOTES TO THE SPECIFIER ARE CONTAINED IN BOXES AND SHOULD BE DELETED FROM FINAL COPY. OPTIONAL ITEMS REQUIRING SELECTION BY THE SPECIFIER ARE ENCLOSED WITHIN BRACKETS, E.G. [35] [40] [45]. MAKE APPROPRIATE SELECTIONS AND DELETE OTHERS. ITEMS REQUIRING ADDITIONAL INFORMATION ARE UNDERLINED BLANK SPACES, E.G. ___________ . OPTIONAL PARAGRAPHS AND FEATURES THAT MAY BE SELECTED OR DELETED AS DESIRED ARE SHOWN IN BOLD FACE TYPE. CONVERT THE BOLD FACE TYPE TO REGULAR TYPE WHEN INCLUDING THESE PARAGRAPHS OR FEATURES; DELETE THEM IF NOT REQUIRED FOR THE PROJECT. revise footer to suit project/office requirements. ELECTRONIC VERSIONS OF THIS SPECIFICATION UTILIZE AUTOMATIC PARAGRAPH NUMBERING. WHEN EDITING IS COMPLETE, DELETE ALL TEXT ON THIS PAGE, THEN REMOVE THE SECTION BREAK AT THE TOP OF THE NEXT PAGE TO REMOVE THIS PAGE FROM THE DOCUMENT.

SPECIFICATION BEGINS ON THE FOLLOWING PAGE.

Initial Issue Date:	December 10, 2007

Revision 1:	April 11, 2011

Revision 2:	April 17, 2014

Revision 3: 	August 15, 2019

Section 05 59 10

Cable/Rod trellises

# General

## Summary

### Section Includes: [wall mounted] [freestanding] [aluminum framed] trellises with stainless steel [cable and rod] [rod] vine grids.

### Related Sections:

INSERT SECTION NUMBER(S) AND TITLE(S) BELOW FOR WORK TO WHICH TRELLISES WILL BE ANCHORED. VERIFY THAT RELATED SECTIONS ALSO REFERENCE THIS SECTION.

#### __ __ __–_________________________________.

#### __ __ __–_________________________________.

## Submittals

### Reference Section 01 33 00(Submittal Procedures; submit following items:

#### Product Data.

SHOP DRAWINGS MAY NOT BE REQUIRED FOR SMALL, SIMPLE PROJECTS. DELETE FOLLOWING PARAGRAPH IF SHOP DRAWINGS ARE NOT DESIRED.

#### Shop Drawings: Indicate materials, sizes, anchorage and installation details for trellis system.

#### Manufacturer's installation instructions.

#### Special Warranties.

## Delivery, Storage, and Handling

### Reference Section 01 66 00(Product Storage and Handling Requirements.

## Warranty

COMPLETE TEXT OF FOLLOWING WARRANTIES IS AVAILABLE FROM FEENEY UPON REQUEST.

### Special Warranty:

#### Feeney trellises: 5 year limited warranty against defects in material on aluminum support frames and finishes, stainless steel cables, rods and connectors when used for the purpose intended under normal conditions.

# Products

## Manufacturer

### Feeney, Inc.	Toll Free: (800) 888-2418

### 2603 Union St	Tel: (510) 893-9473

### Oakland, CA 94607	Fax: (510) 893-9484

### E-mail: sales@feeneyinc.com

### Website: www.feeneyinc.com

### Product: Feeney® Trellises

### Substitutions: Reference Section 01 63 00(Product Substitution Procedures.

## Components

SELECT PARAGRAPH A. AND/OR B. AND/OR C. BELOW DEPENDING ON PROJECT REQUIREMENTS. DELETE TRELLIS TYPES NOT USED. VERIFY THAT TRELLIS DIMENSIONS ARE SHOWN ON DRAWINGS.  VERIFY THAT DETAILS FOR INSTALLATION/MOUNTING ARE SHOWN ON DRAWING AND APPROVED BY STRUCTURAL ENGINEER.

### Wall Mounted Somerset®-II Trellis:

#### Top Angle Brackets: [Straight Style] [Arch Style], 1-1/2 by 2 by 1/8 inch (38.1 by 50.8 by 3.2 mm) thick powder coated aluminum angles, 40 inches (1,016 mm) long with stand-off blocks; predrilled for mounting hardware and cable installation.

#### Bottom Angle Brackets:  1-1/2 by 2 by 1/8 inch (38.1 by 50.8 by 3.2 mm) thick powder coated aluminum angles, 40 inches (1,016 mm) long with stand-off blocks; predrilled for mounting hardware and cable installation.

#### Cables: 1/8 inch (3.2 mm) diameter, type 316 stainless steel, polished finish, commercial, dry grade; include attachment fittings.

#### Rods: 1/8 inch (3.2 mm) diameter, type 316 stainless steel.

#### Accessories:  As recommended by manufacturer to secure rods and provide finish details, and as shown on Drawings to mount angle brackets.

### Wall Mounted 3-in-1 Trellis:

#### Mounting hardware:  stainless steel 2 inch (50.8 mm) stand-offs support fittings with stainless steel hanger bolts and locking hex nuts.

#### Rods:  1/8 inch (3.2 mm) diameter, type 316 stainless steel.

#### Accessories:  As recommended by manufacturer to secure rods and provide finish details, and as shown on Drawings to mount stand-off support fittings.

#### Installation Design Configuration:  [fan design] [grid design] [diamond design].

### Freestanding Greenway Trellis:

#### Frame: 1-1/2 inch (38.1 mm) OD by 1/8 inch (3.2 mm) wall thickness aluminum tube sections with splice sleeves and locking-screws; predrilled for cable installation.

#### Cables:  1/8 inch (3.2 mm) diameter, type 316 stainless steel, polished finish, commercial, dry grade; include attachment fittings.

#### Rods: 1/8 inch (3.2 mm) diameter, stainless steel.

#### Installation Configuration: [Legs cast in concrete] [Legs set in gravel fill] [Legs secured with aluminum base plates].

DELETE BRACKETED TEXT IN 5. BELOW IF BASE PLATES ARE NOT USED.

#### Accessories: As recommended by Manufacturer to secure rods and provide finish details [and as shown on Drawings to secure with aluminum base plates].

BELOW SECTION 2.03 FINISH ONLY APPLIES TO SOMERSET® II AND GREENWAY TRELLISES. DELETE SECTION IF ONLY USING 3-IN-1 TRELLISES.

## Finish

### Shop Finish: Aluminum components; powder coated per AAMA 2604 paint finishes.

IN ADDITION TO THE COLORS LISTED BELOW, OVER 200 CUSTOM COLORS ARE AVAILABLE.  CONTACT FEENEY, INC. FOR FURTHER INFORMATION.

### Aluminum Components Color: [Black Matte] [Custom color as selected by Architect] [as shown on drawings]

# Execution

## Examination

### Examine work upon which trellis(es) will be installed.

### Coordinate with responsible entity to correct unsatisfactory conditions.

### Commencement of work by installer is acceptance of substrate conditions.

## INSTALLATION

MANUFACTURER’S INSTALLATION INSTRUCTIONS COVER PROCEDURES FOR TYPICAL INSTALLATION CONDITIONS. INSERT ADDITIONAL REQUIREMENTS BELOW AS NECESSARY TO COVER SPECIAL OR UNUSUAL CONDITIONS.

### Follow Manufacturer’s installation instructions.

## Cleaning

### Reference Section 01 74 00(Cleaning and Waste Management.

### Clean powder-coated aluminum surfaces using hot soapy water; rinse thoroughly with clear water and wipe dry.

### Clean all stainless-steel components thoroughly using synthetic, non-scratch pads and hot soapy water (or use stainless steel cleaners & protectants as recommended by Manufacturer) to remove residual lubricants; rinse thoroughly with clear water and wipe dry.

End of Section